## Slide 1: Digital Logic Design
By Amr Al-Awamry
Lecture 10

## Slide 2: Overview
Circuits require memory to store intermediate data
Sequential circuits use a periodic signal to determine when to store values.
  A clock signal can determine storage times
  Clock signals are periodic
Single bit storage element is a flip flop
A basic type of flip flop is a latch
Latches are made from logic gates
  NAND, NOR, AND, OR, Inverter
Notes: credential:
bring a computer
die photo
wafer
:
This can be an hidden slide. I just want to use this to do my own planning.
I have rearranged Culler’s lecture slides slightly and add more slides. This covers everything he covers in his first lecture (and more) but may
We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20.
Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs.

## Slide 3: The story so far ...
Logical operations which respond to combinations of inputs to produce an output.
  Call these combinational logic circuits.
For example, can add two numbers. But:
  No way of adding two numbers, then adding a third (a sequential operation);
  No way of remembering or storing information after inputs have been removed.
To handle this, we need sequential logic capable of storing intermediate (and final) results.

## Slide 4: Sequential Circuits
Combinational circuit
Flip Flops
Outputs
Inputs
Next state
Present state
Timing signal (clock)
Clock
Clock
a periodic external event (input)
synchronizes when current state changes happen
keeps system well-behaved
makes it easier to design and build large systems

## Slide 5: Cross-coupled Inverters
State 1
State 2
A stable value can be stored at inverter outputs

## Slide 6: S-R Latch with NORs
1 1
1 0
0 1
0 0
S R Q Q’
0 1
1 0 Set
1 0
Stable
0 1 Reset
0 0 Undefined
R (reset)
Q
Q
S (set)
S-R latch made from cross-coupled NORs
If Q = 1, set state
If Q = 0, reset state
Usually S=0 and R=0
S=1 and R=1 generates unpredictable results

## Slide 7: S-R Latch with NANDs
S
R
Q
Q’
0 0
0 1
1 0
1 1
S R Q Q’
0 1
1 0 Set
1 0
Store
0 1 Reset
1 1 Disallowed
Latch made from cross-coupled NANDs
Sometimes called S’-R’ latch
Usually S=1 and R=1
S=0 and R=0 generates unpredictable results

## Slide 8
S-R Latches

## Slide 9: S-R Latch with control input
Occasionally, desirable to avoid latch changes
C = 0 disables all latch state changes
Control signal enables data change when C = 1
Right side of circuit same as ordinary S-R latch.

## Slide 10: NOR S-R Latch with Control Input
Latch operation enabled by
C
Input sampling enabled by gates
R’
S’
Q’
Q
C’
Outputs change when C is low:
RESET and SET
Otherwise: HOLD
Latch is level-sensitive, in regards to C
Only stores data if C’ = 0

## Slide 11: D Latch
Q
Q’
C
D
S
R
X
Y
X Y C Q Q’
0 0 1 Q0 Q0’ Store
0 1 1 0 1 Reset
1 0 1 1 0 Set
1 1 1 1 1 Disallowed
X X 0 Q0 Q0’ Store
0 1 0 1
1 1 1 0
X 0 Q0 Q0’
D C Q Q’
Q0 indicates the previous state (the previously stored value)

## Slide 12: D Latch
Q
Q’
C
D
S
R
X
Y
0 1 0 1
1 1 1 0
X 0 Q0 Q0’
D C Q Q’
Input value D is passed to output Q when C is high
Input value D is ignored when C is low

## Slide 13: D Latch
E
x
Latches on following
edge of clock
E
D
Q
C
x
z
z
Z only changes when E is high
If E is high, Z will follow X

## Slide 14: D Latch
E
x
Latches on following
edge of clock
E
D
Q
C
x
z
z
The D latch stores data indefinitely, regardless of input D values, if C = 0
Forms basic storage element in computers

## Slide 15: Symbols for Latches
SR latch is based on NOR gates
S’R’ latch based on NAND gates
D latch can be based on either.
D latch sometimes called transparent latch

## Slide 16: Summary
Latches are based on combinational gates (e.g. NAND, NOR)
Latches store data even after data input has been removed
S-R latches operate like cross-coupled inverters with control inputs (S = set, R = reset)
With additional gates, an S-R latch can be converted to a D latch (D stands for data)
D latch is simple to understand conceptually
  When C = 1, data input D stored in latch and output as Q
  When C = 0, data input D ignored and previous latch value output at Q
Next time: more storage elements!
Notes: credential:
bring a computer
die photo
wafer
:
This can be an hidden slide. I just want to use this to do my own planning.
I have rearranged Culler’s lecture slides slightly and add more slides. This covers everything he covers in his first lecture (and more) but may
We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20.
Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs.